# NATIONALLY ACCREDITED CERTIFICATION SCHEME FOR INDIVIDUAL GAS FITTING OPERATIVES

## GUIDANCE TO ACS GAS SAFETY ASSESSMENT FRAMEWORK

## VERSION 13

Introduction

## This Version 12 of ‘GUIDANCE TO ACS GAS SAFETY ASSESSMENT FRAMEWORK’ replaces all previous versions & now includes new additional details used within the Nationally Accredited Certification Scheme For Individual Gas Fitting Operatives.

The Flow Charts now include:-

- Details of the Competencies contained in the new ‘Generic Format’ used to construct the Initial Assessment Criteria.

- Details of the Competencies contained in the new ‘Generic Format’ used to construct the Re-Assessment Criteria.

- New Changeover Cores to enable easier transfer among differing ‘Industry Gas Sectors’

- Details of the ACS competencies which align with the S/NVQ 6012 Scheme

- Details of the ‘ACS Aligned S/NVQ’ Re-Certification Scheme for Emergency Service Operatives 6012 - 44

###### Legend

INITIAL DOMESTIC GAS SAFETY ACS ASSESSMENTS FLOW CHARTS FOR NATURAL GAS & LPG

|  |  | GENERIC FUEL CHANGEOVER CORE NG to LPG - CoNGLP 1. |
| --- | --- | --- |
|  |  | FUEL CHANGEOVER CORE LPG to NG - CoLPNG 1. |

NATURAL GAS INITIAL CORE COMPETENCIES

# Example 1

#### An operative who installs & commissions, disconnects & repairs natural gas pipe-work only & does not work on any appliances

#### CCN 1.  (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core domestic gas work by Practical and knowledge & understanding means. Applicable to all domestic gas fittings

# Example 2

#### An operative who installs, exchanges, disconnects services, repairs, attends breakdowns & commissions natural gas central heating boilers

#### CCN 1. (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core domestic gas work by Practical and knowledge & understanding means. Applicable to all domestic gas fittings

- CENWAT.

Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair, attends to breakdown  & commission domestic gas central heating boilers & water heaters by Practical and knowledge & understanding means (see flow chart).

- CPA 1. (This assessment is a pre-requisite for CENWAT.)

Designed to test gas safety competence of an operative in the work of carrying out an appliance combustion performance analysis

# Example 3

## Operatives intending to extend their work range from domestic natural gas appliances to include liquefied petroleum gas appliances

## (in permanent dwellings)

- CoNGLP 1. (PD) (Fuel changeover assessment NG to LPG)

Designed to test the gas safety competence of an operative intending to extend the work range from domestic NG appliances to include LPG appliances by practical and knowledge & understanding means.

Note: Before the above assessments can be undertaken, the candidate must hold as a minimum a certificate of competence in Domestic Core Gas Safety CCN 1.

- Appliances already held in NG are automatically given in LPG in conjunction with CoNGLP 1.

- If gas work is to be undertaken in a Residential Park Home then CoNGLP 1. (RPH) should be taken.

Note: All LPG assessments will become invalid if the NG core CCN1. expires

###### Example 4

## An operative intending to extend their work range from domestic liquefied petroleum gas to include natural gas

## CoLPNG 1. (Fuel changeover assessment LPG to NG)

Designed to test the gas safety competence of an operative intending to extend the work range from domestic LPG appliances to include NG appliances by practical and knowledge & understanding means.

Note: Before the above assessments can be undertaken, the candidate must hold as a minimum a certificate of competence in Domestic Core Gas Safety CCLP 1.

- Appliances already held in NG are automatically given in LPG in conjunction with CoNGLP 1.

INITIAL DOMESTIC GAS SAFETY ASSESSMENTS LIQUEFIED PETROLEUM GAS FLOW CHART FOR

SPECIFIC LPG SECTORS (ASSESSMENT BANK B)

LIQUEFIED PETROLEUM GAS GENERIC CORE COMPETENCIES

Example 1

#### An operative who installs, exchanges, disconnects, services, repairs, attends to breakdown & commissions liquefied petroleum gas pipe-work & closed flue gas fires in caravan holiday homes (LAV)

#### CCLP 1. (LAV) (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core domestic Caravan LPG gas work by practical and knowledge & understanding means.

- HTRLP 2. Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair breakdown & commission closed flue LPG gas fires in leisure accommodation vehicles by practical and knowledge & understanding means.

# Example 2

#### An operative who installs, exchanges, disconnects services, repairs, attends to breakdown & commissions liquefied petroleum gas water heaters in

#### touring & motorised caravans (LAV - Leisure Accommodation Vehicles)

#### CCLP 1. (LAV) (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core domestic Caravan LPG gas work by practical and knowledge & understanding means.

- WATLP 2. Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair breakdown & commission LPG water heaters designed for use in touring & motorised caravans by practical and knowledge & understanding means.

# Example 3

#### An operative who installs, exchanges, disconnects services, repairs, attends to breakdown & commissions liquefied petroleum gas cookers & warm air heaters installed on boats (B)

#### CCLP 1. (B) (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core domestic Boat LPG gas work by practical and knowledge & understanding means

##### CKR 1. Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair, attends to breakdown  & commission domestic LPG gas cooking appliances by practical and knowledge & understanding means

WAHLP 1. Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair, attends to breakdown  & commission domestic LPG gas boat warm air heating systems by practical and knowledge & understanding means

###### Example 4

## An operative who installs & commissions single supply polyethylene external underground liquefied petroleum gas pipe-work & gas vessel connections (EP)

- CCLP 1. (EP)  (Core/ pre-requisite) Designed to test the gas safety competence of an operative in core domestic external pipework LPG gas work by practical and knowledge & understanding means.

- VESLP 1.  Designed to test the gas safety competence of an operative in the work of gas storage vessel connections, controls and safety requirements. Sizing external above ground and un-jointed below ground pipe-work of up to 0.02m³ for single LPG gas supplies by Practical and knowledge & understanding means

INITIAL NON DOMESTIC/COMMERCIAL GAS SAFETY ACS ASSESSMENTS FLOW CHART

INITIAL NON DOMESTIC/COMMERCIAL GAS SAFETY ACS ASSESSMENTS TITLES

Non Domestic/Commercial Pipework Assessments                       Non Domestic/Commercial Heating Assessments

Non Domestic/Commercial Catering Assessments                        Non Domestic/Commercial Laundry Assessments

# Non Domestic/Commercial Miscellaneous Assessments

# Commercial Catering Assessment Content Table

* Appliances marked bold with an asterisk at the top of each Table are the appliances used for assessment, providing evidence of competence for other appliances listed below in each table.

# Example 1

An operative who installs commercial pipe work up to 16 bar pressure, tests & purges & installs, services, repairs, attends to breakdowns & commissions commercial indirect fired natural gas appliances

- PART A. – Generic Non-Domestic Assessment Core Common Competencies 1-5

- PART B. - Generic Non-Domestic Assessment Core Commercial Appliances Common Competencies 6-11

- COCN 1. (PART C) – Specific Core Commercial Heating Common Competencies 12-14, Designed to test the gas safety competence of an operative in

core commercial heating

- TPCP 1.  -  Designed to test the gas safety competence of an operative in strength/tightness testing and direct purging of commercial pipe work up to

16 bar pressure.

- ICPN 1.  – Designed to test the gas safety competence of an operative in installing commercial pipe work above 35mm in diameter.

(Not PE Electro-Fusion)

- CIGA 1.  – Designed to test the gas safety competence of an operative in install, commission, service, repair & breakdown of indirect fired commercial

appliances.

##### Example 2

###### An operative who installs, services, repairs, attends to breakdowns & commissions commercial overhead radiant & tube heaters on natural gas

- PART A. – Generic Non-Domestic Assessment Core Common Competencies 1-5

- PART B. - Generic Non-Domestic Assessment Core Commercial Appliances Common Competencies 6-11

- COCN 1. (PART C) – Specific Core Commercial Heating Common Competencies 12-14, Designed to test the gas safety competence of an operative in

core commercial heating

- ICPN 1. – Designed to test the gas safety competence of an operative in installing commercial pipe work above 35mm in diameter.

(Not PE Electro-Fusion)

- CORT 1.  - Designed to test the gas safety competence of an operative in the work of commission, service, repair and breakdown of commercial

overhead luminous radiant plaque and radiant tube heaters.

### Example 3

A pipe fitter who installs, tests and purges natural gas commercial pipe-work up to 1m³ volume, working at up to 40mb operating pressure (OP) and not exceeding 150mm/6" diameter

- COCNPI 1LS. (PART A.) – Generic Non-Domestic Assessment Core Common Competencies 1-5  (Core/pre-requisite for Pipe Installer/Commissioner)

- ICPN 1. - Designed to test the gas safety competence of an operative in installing commercial pipe work above 35mm in diameter.

(Not PE Electro-Fusion)

- TPCP 1A. Designed to test the gas safety competence of an operative in strength/tightness testing and direct purging of commercial pipe-work up to 1m³volume at up to 40mbar OP.

### Example 4

A pipe fitter who only installs natural gas commercial pipe-work up to 150mm/6"diameter that is not connected to a gas supply

- ICPN 1LS. (Stand alone assessment no pre-requisite core assessment needed) Designed to test the gas safety competence of an operative in first

fixing of commercial installation pipe-work but does not connect to a live gas supply.

# Example 5

#### An operative who installs, services, repairs, attends to breakdowns & commissions any natural gas catering appliance covered by COMCAT1

- PART A. – Generic Non-Domestic Assessment Core Common Competencies 1-5

- PART B. - Generic Non-Domestic Assessment Core Commercial Appliances Common Competencies 6-11

#### CCCN 1. (PART C) – Specific Core Commercial Catering Common Competencies 12-13, (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core commercial catering.

##### COMCAT 1. - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair,

##### breakdown & commission of catering appliances in COMCAT 1 grouping (See Table page 8) by Practical & knowledge & understanding

###### Example 6

An operative intending to extend the work range from commercial catering natural gas to commercial catering liquefied petroleum gas holding CCCN1. or equivalent with COMCAT assessments.

### CoNGLP 1. (PART D) – Specific Core Fuel changeover NG to LPG competencies 1 – 6.  Designed to test the gas safety competence of an operative

### intending to extend the commercial catering work range from natural gas to include LPG.

- (PD) – (PART E) FOR - Specific Core Fuel changeover NG to LPG for Permanent Dwellings competencies 7 – 9

- (CMC) – (PART F) FOR - Specific Core Fuel changeover NG to LPG for Mobile Catering competencies 12 - 14

Note:  Appliances already held in NG are automatically given in LPG in conjunction with CoNGLP 1. (PD) or CoNGLP1CMC

# Example 7

#### An operative who installs, services, repairs, attends to breakdown & commissions any LPG commercial mobile catering appliance from CMCALP 2.

- PART A. – Generic Non-Domestic Assessment Core Common Competencies 1-5

- PART B. - Generic Non-Domestic Assessment Core Commercial Appliances Common Competencies 6-11

#### CCCN 1. (PART C) – Specific Core Commercial Catering Common Competencies 12-13, (Core /pre requisite assessment)

##### Designed to test the gas safety competence of an operative in core commercial catering.

- COMCAT 3. - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service, repair,

breakdown & commission of catering appliances in COMCAT 3 grouping (See Table page 8) by Practical, knowledge & understanding.

### CoNGLP 1. (PART D) – Specific Core Fuel changeover NG to LPG competencies 1 – 6.

- (CMC) – (PART F) FOR - Specific Core Fuel changeover NG to LPG for Mobile Catering competencies 12 - 14

ACS DOMESTIC/NON DOMESTIC/COMMERCIAL INITIAL CHANGEOVER ASSESSMENTS FLOW CHART

Example 1

An operative intending to extend work range from domestic natural gas appliances to include non-domestic/commercial heating appliances across range

- PART A. – Generic Changeover Assessment Domestic Natural Gas to Common Commercial Appliance Core Competencies 1-6

- Specific PART B. CoDNCO1. – Specific Commercial Heating Core Competencies 7-9

- CORT1. - Designed to test the gas safety competence of an operative in the work of commission, service, repair and breakdown of commercial

overhead luminous radiant plaque and radiant tube heaters

- CIGA1. - Designed to test the gas safety competence of an operative in install, commission, service, repair & breakdown of indirect fired commercial

appliances.

- CDGA1. - Designed to test the gas safety competence of an operative in install, commission, service, repair & breakdown of direct fired commercial

appliances.

Example 2

## Operatives intending to extend their work range from domestic natural gas appliances to include commercial natural gas catering appliances covered by COMCAT 1 & COMCAT 3. Table 1 & 3.

- PART A. – Generic Changeover Assessment Domestic Natural Gas to Common Commercial Appliance Core Competencies 1-6

- SPECIFIC PART B. CoDC 1. – Specific Commercial Catering Core Competencies 7-9

##### CoCATA 1. - Designed to test the gas safety competence of an operative intending to extend the work range from domestic NG appliances to include

##### commercial NG catering appliances by Practical and knowledge & understanding means. Applicable to all commercial catering contained in COMCAT’s 1 & 3 (See Table page 10)

##### *Note: Before the above Changeover assessments can be undertaken, the candidate must hold as a minimum a certificate of competence in Domestic Core

##### Gas Safety CCN 1. & appropriate Domestic appliance assessments such as CKR 1. – WAT 1.

Example 3

Operatives intending to extend their work range from domestic natural gas appliances to include commercial natural gas laundry appliances & the installation testing & purging of low pressure commercial pipework.

- PART A. – Generic Changeover Assessment Domestic Natural Gas to Common Commercial Appliance Core Competencies 1-6

- SPECIFIC PART B. CoCCLNG1. – Specific Commercial Laundry Core Competencies 7-8

- CLE1.  -  Designed to test the gas safety competence of an operative in the work of commission, service, repair and breakdown of commercial

laundry appliances.

- ICPN1. - Designed to test the gas safety competence of an operative in installing commercial pipe work above 35mm in diameter.

(Not PE Electro-Fusion)

- TPCP1A. Designed to test the gas safety competence of an operative in strength/tightness testing and direct purging of commercial pipe-work up to 1m³volume at up to 40mbar OP.

INITIAL EMERGENCY SERVICE OPERATIVES & GAS METER INSTALLERS NATURAL GAS ASSESSMENTS

INITIAL EMERGENCY SERVICE OPERATIVES & GAS METER INSTALLERS

ACS GENERIC ASSESSMENTS

CMA 3 DOMESTIC GAS METER INSTALLER ASSESSMENT

Domestic Gas Meter Installer CMA 3 (Including Installation and commissioning of domestic pipework )

MET 1 (Only Meter Assessment option)

REGT 1 (Only MP Regulator option)

# Example 1

An AMI approved meter installer who installs domestic natural gas meters to low pressures supplies with a MP Option

- CMA 3 - Generic Core designed to test the gas safety competence of an operative in core domestic meter gas work by practical & knowledge & understanding means.

- MET 1. - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service & commission domestic gas meters up to U6 in size by practical and knowledge & understanding means.

Option

- REGT 1. - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service & commission medium pressure service regulators.

# Example 2

An AMI approved meter installer who installs low pressure non domestic natural gas diaphragm meters up to U40 size, natural gas meters diaphragm meters with by-passes, RPD meters & medium pressure Turbine meters.

- CMA 1. - Generic Core designed to test the gas safety competence of an operative in core domestic meter gas work by practical & knowledge & understanding means.

- MET 4.  - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service & commission domestic/small commercial gas meters up to U40 in size using anacondas by practical and knowledge & understanding means.

- ICPN 1. - Designed to test the gas safety competence of an operative in installing commercial pipe work above 35mm in diameter.

- REGT 2.- Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service & commission medium pressure service regulators.

- TPCP 1.  -  Designed to test the gas safety competence of an operative in strength/tightness testing and direct purging of commercial pipe work up to 16 bar pressure.

- CMET 1.  - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service & commission non-domestic gas meters both of large diaphragm meters with by-pass & RPD meters by practical and knowledge & understanding means.

- CMET 2. - Designed to test the gas safety competence of an operative in the work of install, exchange, disconnect, service & commission non-domestic/commercial gas meters both of RPD & Turbine types by practical and knowledge & understanding means.

Note: Holders of assessment MET4. Are also competent to meet the requirements of MET2.

Example 3

An approved gas emergency service operative responding to public reported escapes

- CESP 1. – Generic Core designed to test the gas safety competence of an operative in the work of an emergency service provider

Note: In addition to the above generic core the operative will have to successfully complete additional upstream training & assessment provided by the employer. 	(See appendix 2 - ACS Assessments for ESP’s)

Example 4

An operative employed by a Gas Meter Asset Manager to install correctors & other instrumentation to Non-Domestic/Commercial Meters

- CMIT 1. - Generic Core designed to test the gas safety competence of an instrumentation operative in core non-domestic/commercial meter gas work by practical & knowledge & understanding means.

ASSESSMENT for DOMESTIC NATURAL GAS

DOMESTIC LIQUEFIED PETROLEUM GAS RE-ASSESSMENT CRITERIA

EMERGENCY SERVICE OPERATIVES & GAS METER INSTALLERS ACS RE- ASSESSMENTS

VARIATIONS TO STANDARD ACS ASSESSMENT COMBINATIONS

A number of ACS Assessment Criteria were originally placed in the ‘Gas Sector Criteria’ that was most appropriate at the time of publication. Since then it has become apparent that some of these assessment criteria can be utilised effectively across a wider range of gas sectors without the need of the originally identified pre-requisites.

Listed below are some of the more common variations that an operative can make use of to ensure that they are holding the necessary certificate of competence by following an acceptable alternative route.

WHAT’S THE ANSWER?

This page is intended to give some guidance to anyone involved in offering advice to operatives intending to undertake ACS assessments.

# The following examples of typical questions/response should be used in conjunction with the attached flowcharts.

Candidates Questions				     Response				 Candidates Questions			         Response

# Text boxes

# All assessment details in green boxes containing writing in black & black edged are suitable for natural gas only	                                         NG

#### NG

Arrow

##### LPG Arrow

Arrow

# All assessment details in orange boxes containing writing in black & black edged are suitable for liquefied petroleum gas only                             LPG

Changeover

Arrow

## All assessment details in green boxes containing writing in orange & orange edged are suitable for both NG & LPG                                      NG & LPG

# All assessment details in yellow boxes containing writing in black & black edged are changeover assessments only

# All purple boxes contain additional information

Linkage

Arrow

## CORE DOMESTIC GAS SAFETY

ASSESSMENT

NATURAL GAS

CCN 1.

GENERIC LPG CORE Parts A & B

DOMESTIC GAS SAFETY ASSESSMENT
LIQUEFIED PETROLEUM GAS CCLP 1.

Both the Generic LPG main core Parts A (CCLP1.) & LPG Changeover Core (CoNGLP1.) needs the additional support of Specific Part B LPG Sectors i.e. Permanent dwellings (PD).

Residential Park Homes (RPH). Leisure Accommodation Vehicles (LAV).

Boats (B)

APPLIANCE ASSESSMENT BANK A.

GAS COOKERS                                                    CKR 1.      NG & LPG

Operatives already holding a Domestic Core & appliances with one fuel who successfully complete a fuel changeover will be competent to work on those appliances in both fuels with certificates issued accordingly.

OPERATIVES CAN SELECT APPLIANCE ASSESSMENTS FROM THESE DOMESTIC APPLIANCES APPROPRIATE TO EACH LPG SECTOR

OPERATIVES CAN SELECT APPLIANCE ASSESSMENTS FROM THESE DOMESTIC APPLIANCES APPROPRIATE TO EACH NG SECTOR

The appropriate “Core”

NG or LPG

or both is a

pre-requisite for all of these appliance assessments.

Appliance assessments

must be selected to cover the areas of work

undertaken by

operatives

GAS FIRES/HEATERS 			        HTR 1.      NG & LPG

CENTRAL HEATING/WATER HEATERS                    CENWAT   NG &LPG

LAUNDRY APPLIANCES 			        LAU 1.        NG & LPG

WATER HEATERS                                                                           WAT 1       NG &LPG

DUCTED AIR HEATERS 			        DAH 1.       NG & LPG

LEISURE EQUIPMENT 			        LEI 1.          NG & LPG

DOMESTIC GAS METERS 			        MET1 & 2. NG & LPG

RANGE - COOKER BOILERS 		        CKHB 1.   NG & LPG

WATER BOILERS (Swimming Pool)	        HWB 1.     NG & LPG

FORCED DRAUGHT GAS BURNERS                 DFDA 1.    NG & LPG

ATMOSPHERE SAMPLING CO & CO2                      CMDDA 1. NG &LPG

CORE COMPETENCIES CCN 1.

- Gas Safety Legislation.

- Gas Emergency Actions and Procedures.

- Products & Characteristics of Combustion.

- Ventilation.

- Installation of Pipework and Fittings.

- Testing for Tightness.

- Checking and/or Setting Meter Regulators.

- Identification of Unsafe Situations and the Use of Emergency Notices and Warning Labels.

- The Operation of and Positioning of Emergency Isolation Controls and Valves.

- Checking and Setting Appliance Burner Pressures and Gas Rates.

- The Operation and Checking of Appliance Gas Safety Devices and Controls.

- Chimney Standards.

- Chimney Testing.

- Installation of Open, Balanced and Fan Assisted  Chimney Configurations

- Re-establish Existing Gas Supply and Relight Appliances.

GENERIC CORE CHANGEOVER COMPETENCIES NG to LPG CoNGLP 1.

1      Characteristics of Liquefied Petroleum Gas.

2.     Cylinder Location Safety Requirements and Sizing

3.     LPG Supply Pressures – Operation of and Positioning of Emergency Isolation, Flow Control and Valves for Cylinders.

4.     Gas Emergency Actions and Procedures

5      Installation of pipework and fittings for LPG

6.    Testing for Soundness installation pipework with total internal volume as per BS5482 pt 1 (TM83) & operating pressure up to 37 mbar - applies to (PD), (LAV) and (RPH).                         And/or

Testing for Soundness for LPG Installations in Boats, Yachts/ Vessels (B).

NB. Additional competencies are required for specific LPG Sectors i.e. PD, LAV, RPH, B, EP, EPC. (See LPG Charts)

CORE CHANGEOVER COMPETENCIES LPG to NG CoLPNG 1.

1      Gas Emergency Actions and Procedures - Including characteristics of NG.

2.     Ventilation - Related to NG.

3.     Installation of Pipework and Fittings - Related to NG.

4.     Identification of Unsafe Situations and the Use of Emergency Notices

5     Testing for Tightness

6.    Checking and/or Setting Meter Regulators

7.    The Operation of and Positioning of Emergency Isolation Controls and Valves

8.    Checking and Setting Appliance Burner Pressures and Gas Rates

9.    Chimney Standards - Related to NG

10.  The Installation of Open, Balanced and Fan Assisted Flue Assemblies for Natural Gas Appliances

*SEE FLOW CHART DOMESTIC ASSESSMENTS

*SEE FLOW CHART DOMESTIC ASSESSMENTS

*SEE FLOW CHART DOMESTIC ASSESSMENTS

*SEE FLOW CHART DOMESTIC ASSESSMENTS

LIMITED SCOPE

SPECIFIC ASSESSMENT

Group 3

Competencies

For:-

LPG EXTERNAL PIPEWORK CONNECTIONS

Domestic &

Small Commercial

*CCLP1. (EPC)

## GENERIC LIQUEFIED PETROLEUM GAS CORE CCLP1.

## Group 1 Part A (Must be joined from a sector code below)

Common Core Competencies For All LPG Sectors:-

## (PD)  -   Permanent Dwellings – Domestic, Commercial & Catering Establishments

### (LAV) – Leisure Accommodation Vehicles

(RPH) – Residential Park Homes

(B)   -     Boats, Yachts & Other Vessels

Limited Scope

Specific Sector Core

Group 2

Part A (EP)

Competencies

For:-

LPG EXTERNAL PIPEWORK

CCLP1. (EP)

Limited Scope

Specific Sector Core

Group 2

Part A (MC)

Competencies

For:-

LPG Cabinet Heaters/Leisure Equipment

CCLP1. (MC)

The appropriate sector code needs to be added after the Core Assessment Ref. No. to cover the sector which the operative is involved with e.g.CCLP1. (PD)

This assessment above is suitable for operatives who install PE pipework for below ground natural gas outlet supplies & may stand alone without any Core Assessment for operatives who DO NOT connect to a live gas supply or commissions the newly installed pipe work.

Selected Appropriate Domestic Appliance Assessments From Page 4 Assessment BANK A. (E.G. CKR1. – CEN1. – HTR1. – WAT1.) or Appropriate Specific LPG Sector Appliances From Assessment Bank B. (Below)

Group 1 Part B

Specific Sector

Core Competencies

For Boats, Yachts & Other Vessels

CCLP1. (B)

Group 1 Part B

Specific Sector

Core Competencies

For Leisure Accommodation Vehicles

CCLP1. (LAV)

Group 1 Part B

Specific Sector

Core Competencies

For Residential Park Homes

CCLP1. (RPH)

Group 1 Part B

Specific Sector

Core Competencies

For Permanent Dwellings

CCLP1. (PD)

* Operatives requiring to test & commission pipework installed under

VESLP2.or

CCLP1. (EPC)

with volumes greater than those allowed in BS 5482 Pt.1 will

also require Assessment TPCP1,

Group 2

Additional Assessments Required From:-

CABLP1.

LEILP1.

Group 2

Additional Assessments Required From: -

VESLP1.

* VESLP2.

EFJLP1.

No Further Options for these Groups

##### SINGLE SUPPLY BELOW GROUND PIPEWORK        VESLP 1.  LPG

##### MULTIPLE SUPPLIES BELOW GROUND PIPEWORK   VESLP 2. LPG

##### CLOSED FLUE GAS FIRES         HTRLP 2. LPG

POLYETHYLENE ELECTRO FUSION JOINTING EFJLP 1. NG& LPG

MOBILE CABINET HEATERS 		                 CABLP 1.   LPG

##### CARAVAN SPACE HEATERS      HTRLP 3. LPG

CARAVAN REFRIGERATORS     REFLP 2. LPG

BOAT WARM AIR HEATERS      WAHLP 1. LPG

CARAVAN WATER HEATERS     WATLP 2. LPG

GROUP 2 Part A (EP)

1. Vessel Location & Safety Requirements

2. Supply Pressures, Emergency/Flow controls

3. Emergency Actions & Procedures

4. Legislation

5. Installation of External Pipework/Fittings

6. Identification of Unsafe Situations.

GROUP 1 PART A. GENERIC COMPETENCIES

1.     Characteristics of Liquefied petroleum Gas

2.     Cylinder Location, Safety Requirements & Sizing

3.     LPG Supply Pressures, Operation of & Positioning of ECV’s

4.     Gas Emergency Actions & Procedures

5.     Identification of Unsafe Situations & Use of Emergency Notices

6.     Installation of Pipework & Fittings

7i.    Soundness Test LPG installation pipework volume as per BS 5482 pt 1

(TM 83) & Operating Pressures of up to 37mbar

7ii.   Soundness Test LPG installations in Boats, Yachts & other Vessels

8.     Liquefied Petroleum Gas Safety Legislation

9.     Characteristics Of Combustion of LPG

10.   The Operation & Checking of LPG Appliance Safety Devices/Controls

11.   Flueing Standards for LPG Appliances

12.   Flue Testing

13.   The installation of Open, Closed, Balanced & Fan Assisted Flue Assemblies

14.   Re- Establishing Existing LPG Supplies & Re-lighting Appliances

GROUP 3 (EPC)

1.   Vessel Location & Safety Requirements.

2.   LPG Storage Vessels & Connections.

3.   LPG Supply Pressure (Propane) Operation/Positioning of

Emergency Isolation, flow Controls & Valves.

4.   Gas Emergency Actions & Procedures.

5.   LPG Gas Safety Legislation.

6.    Installation of Service Pipework, Meters/Fittings Alteration of Existing

Installation Pipework (Copper/Steel 6- 28mm, MDPE 32mm).

- Identification of Unsafe Situations/Use of Emergency Notices & Warning

Labels with LPG Gas Installations.

8.    Soundness Testing of LPG Service & Installation Pipework.

9.   Characteristics of LPG.

10. Products & Characteristics of Combustion.

11. Flueing/Chimney Standards.

12. Ventilation.

13. Re-Establish Existing LPG Supplies & Re-Light Domestic/Commercial

Appliances.

SPECIFIC CORE COMPETENCIES GROUP 1 PART B

15.    LPG Supply Pressures, Operation of & Positioning of Emergency & Flow

Control Valves for Bulk Gas Storage Vessels

16.    Cylinder Locations & Safety Requirements

17.    Installation of LPG Pipework & Fittings

18.    Ventilation Requirements for LPG Appliances

19.    Flueing Standards for LPG

20.    Flue Testing for LPG

21.    Flue assemblies for LPG Appliances

22.    Re- Establishing Existing LPG Supplies & Re-lighting Appliances

GROUP 2. Part A. (MC)

1. Cylinder locations & Safety Requirements

2. Characteristics of combustion - LPG

3. Emergency Actions & Procedures

4. Ventilation Requirements

5. LPG Safety Legislation

6. Installation of Pipework/Fittings

7. Identification of Unsafe Situations.

8. Characteristics of LPG

9. LPG Supply pressures

NB. The 8 Competencies within these Specific Core Competencies must use the correct nuances for the Sector being assessed.

e.g.  (PD), (RPH), (LAV), or (B).

*SEE FLOW CHART SPECIFIC

*SEE FLOW CHART SPECIFIC

*SEE FLOW CHART SPECIFIC

*SEE FLOW

CHART SPECIFIC

There are no pre-requisites for the 2 assessments below which are designed for operatives who do not connect to a live gas supply

GENERIC NON-DOMESTIC ASSESSMENT CORE Part A

Common Competencies

GENERIC NON-DOMESTIC ASSESSMENT CORE Part B

Commercial Appliances Common Competencies

* N.B. The use of combustion analysis equipment does not apply to Commercial Laundry

Limited Scope

First Fix Commercial Pipework

ICPN 1LS.

Limited Scope

First Fix Commercial

Appliances

ICAE 1LS.

CCCN 1.

Commercial Catering

Specific Part C. Core Competencies

+ a minimum of 1

assessment from

COMCAT 1.–COMCAT 2.

COMCAT 3.–COMCAT 4.

COMCAT 5.

COCN 1.

Commercial Heating

Specific Part C. Core Competencies

+ a minimum of 1 assessment from

CORT 1. – CIGA 1.

CDGA 1. – CGFE 1.

CCP 1. –BMP1.

CCLNG 1.

Commercial Laundry

Specific Part C. Core Competencies

+ The assessment

CLE 1.

COCNPI 1LS.

Pipe Installer Commissioner

Assessments

Must Include

ICPN 1.

TPCP 1A. & or

TPCP 1.

Additional Options

ICPN 1. – TPCP 1. /1A.

Changeover Core Assessment NG to LPG. CoNGLP1 Specific Part D Core Competency

Changeover Assessment

To Mobile Catering

(CMC)

Specific PART F Core Competency

N.B Must be linked to CoNGLP1CMC

Additional

Option

EFJLP 1.

Additional Options

ICPN 1. – TPCP 1. /1A.

CGLP1,

Additional Options

BMP 1. - EFJLP 1.

* CGFE 1.

Additional Options

ICPN1.-EFJLP1.-CGLP1.

HWB1.–TPCP1. /1A.

* CGFE 1.

When supported with this core, only engines in separate enclosures are covered

Changeover Assessment

To Permanent Dwellings (PD)

CoNGLP1. (PD)

Specific PART E

Cores

OVERHEAD RADIANT & TUBE HEATERS            includes ICAE1.    CORT 1.     NG & LPG

COMMERCIAL PIPEWORK IN EXCESS OF 35mm                                                         ICPN 1.    NG & LPG

STRENGTH, TIGHTNESS TESTING & PURGING PIPEWORK up to 16 bars 	          TPCP 1.   NG & LPG

DIRECT FIRED COMMERCIAL APPLIANCES      includes ICAE1.    CDGA 1.      NG & LPG

INDIRECT FIRED COMMERCIAL APPLIANCES 	includes ICAE1.      CIGA 1.      NG & LPG

STRENGTH/TIGHT/TESTING & PURGING PIPEWORK up to 40mbar & 1m³ volume    TPCP 1A.      NG

GAS FUELLED ENGINES                                   includes ICAE1.     CGFE 1.     NG & LPG

GAS BOOSTERS & ASSOCIATED CONTROLS 				             BMP 1.       NG

Open/Solid Top Ranges 		                                         COMCAT 1.  NG & LPG

COMMERCIAL LAUNDRY EQUIPMENT                                     CLE 1.    NG & LPG

Water Boilers Pressure/STEAM TYPE		            COMCAT 2.  NG & LPG

COMMISSIONING COMMERCIAL PLANT & EQUIPMENT         CCP 1.      NG & LPG

Deep Fat & Pressure Fryers		                            COMCAT 3.  NG & LPG

Fish & Chip ranges 			                                              COMCAT 4.   NG & LPG

* Pressure Type Water Boiler (Stills or equivalent)

Pressure Steamers

Pressure Steaming Ovens

Ancillary Equipment

COMCAT 2.

Appliances Covered

*Open/Solid Top Range

Boiling Burners

Stockpot stoves

Hotplates, Warming Ovens

Bain Marie Hot Cupboards

Combination Ovens

Forced & Natural Convection

Direct & Semi-Indirect Ovens

Boiling Pans Direct/Indirect

Bulk Liquid & Jacketed Urns

Expansion Type Water Boilers

Gas Fired Dishwashers

Gas Heated Rinsing Sinks

Ancillary Equipment

COMCAT 1.

Appliances Covered

* Fish & Chip Ranges

These appliances are normally assembled on site to meet shop front requirements.

COMCAT 4.

Appliances Covered

Forced Draught Burner Appliances                                       COMCAT 5.   NG & LPG

SMALL GAS FIRED Generators 	                                      CGLP 1.        LPG

COMCAT 3.

Appliances Covered

COMCAT 5.

Appliances Covered

NB. CMCALP1, 2, 3. are no longer available, the appropriate COMCAT assessment indicated above should be taken.

*Deepfat & Pressure fryers

Bratt Pans, Griddles, Grills -

Salamanders, Simulated Charcoal, Over/Under fired.

Ancillary Equipment

*Forced Draught Burners

Appliances covered by assessments COMCAT 1-2-3 fitted with forced draught burners need this assessment

*SEE FLOW CHART

NON DOMESTIC ASSESSMENTS

*SEE FLOW CHART

NON DOMESTIC ASSESSMENTS

*SEE FLOW CHART

NON DOMESTIC ASSESSMENTS

*SEE FLOW CHART NON DOMESTIC ASSESSMENTS

*SEE FLOW CHART

NON DOMESTIC ASSESSMENTS

*SEE FLOW CHART

NON DOMESTIC ASSESSMENTS

*SEE FLOW CHART

NON DOMESTIC ASSESSMENTS

Natural Gas

Non Domestic/Commercial Cores

Natural Gas &

Liquefied Petroleum Gas

Non Domestic/Commercial Cores

Changeover Core NG to LPG CoNGLP1.

Domestic Natural Gas Core CCN1.

Part A. Generic Changeover from Domestic Natural Gas to Common Commercial Criteria Competencies 1-6

Changeover

Commercial Heating Core CoDNCO1.

Specific Part B. Competencies

Changeover

Commercial Laundry Core CoCCLNG1.

Specific Part B.

Competencies

Changeover

Commercial

Any Sector

CCCN1.

COCN1.

CCLNG1.

To

Domestic Natural Gas

CoCDN1.

Changeover

Commercial Catering Core CoDC1.

Specific Part B.

Competencies

Changeover Commercial Catering Appliances

CoCATA 1,

Covers COMCAT 1. & COMCAT 3.

Commercial Heating

Appliances from:-

CIGA1.

CDGA1.

CORT1.

BMP1.

CGFE1.

Commercial Laundry

Appliances from:-

CLE1.

Additional Commercial Catering Appliances

From:-

COMCAT2.

COMCAT4.

COMCAT5.

Commercial Pipework

Selected as required

ICPN1.

EFJLP1.

TPCP1A. (NG Only)

TPCP1.

Commercial Pipework

Selected as required

ICPN1.

EFJLP1.

TPCP1A. (NG Only)

TPCP1.

Commercial Pipework

Selected as required

ICPN1.

EFJLP1.

TPCP1A. (NG Only)

TPCP1.

*SEE FLOW CHART

DOMESTIC TO

NON-DOMESTIC

CHANGEOVER ASSESSMENTS

*SEE FLOW CHART

DOMESTIC TO

NON-DOMESTIC

CHANGEOVER ASSESSMENTS

*SEE FLOW CHART

DOMESTIC TO

NON-DOMESTIC

CHANGEOVER ASSESSMENTS

LIMITED SCOPE

GAS METER

Instrumentation

Operative

Contains own core

# LIMITED SCOPE

METER INSTALLER

Generic Competencies

COMMERCIAL PIPEWORK in Excess of 35mm                                                                      ICPN 1.

##### EMERGENCY SERVICE

###### OPERATIVES

COMMERCIAL GAS METER INSTALLER

DOMESTIC / SMALL COMMERCIAL METER INSTALLER

(Up to U40 Size)

DOMESTIC METER
INSTALLER

(Up to U6 Sizes)

Operatives requiring to extend to commercial meters need to hold domestic/small commercial meters MET4. & REGT2.

CESP1.is an alternative Core to CMA 1. Generic Competencies

## STRENGTH/TIGHTNESS TESTING & PURGING COMMERCIAL PIPEWORK TPCP1A & / or TPCP1.

DOMESTIC GAS MEDIUM PRESSURE REGULATORS & CONTROLS                                REGT 1.

DOMESTIC GAS MEDIUM PRESSURE REGULATORS & CONTROLS                                 REGT 1.

GAS SAFETY ASSESSMENT INSTRUMENTATION OPERATIVE Limited Scope                 CMIT 1.

DOMESTIC GAS METERS WITH SEALED OUTLET (Limited Scope) U6                          MET 3LS.

(Limited Scope) METER INSTALLER CORE GAS SAFETY ASSESSMENT NG.              CMA 2LS.

STRENGTH /TIGHTNESS TESTING & PURGING COMMERCIAL PIPEWORK up/to 1m³ TPCP 1A.

STRENGTH /TIGHTNESS TESTING & PURGING COMMERCIAL PIPEWORK up/to 16 bar TPCP 1.

COMMERCIAL RPD & TURBINE METERS                                                                              CMET 2.

### COMMERCIAL DIAPHRAGM & RPD METERS WITH BY-PASS                                             CMET 1.

COMMERCIAL GAS MEDIUM PRESSURE REGULATORS & CONTROLS                        REGT2. 2.

DOMESTIC/COMMERCIAL METERS up to & including U6 to U 40 size                               MET 4.

METER INSTALLER CORE GAS SAFETY ASSESSMENT NG.                                                CMA 3.

METER INSTALLER CORE GAS SAFETY ASSESSMENT NG.                                                CMA 1.

DOMESTIC METERS up to & including U6 size                                                                      MET 1.

## APPENDIX 2 Assessment Delivered by Emergency Service Provider ISBN: 0- 9524550- 7--2

EMERGENCY CORE GAS SAFETY ASSESSMENT NG.                                                        CESP 1.

OR

CHANGEOVER ASSESSMENT DOMESTIC NG TO EMERGENCY CORE                    CoDNESP 1.

Not

ACS

As Required

Generic Initial Assessment Core

Competencies

Non/Dom Pipe

ICPN 1.

Testing up/to 16 bar

TPCP 1.

Testing up/to 1m³

TPCP 1A

Dom/Com Meter

MET 4.

Medium Pressure

REGT 1.

Domestic Meter

MET 1.

Additional Options

With CESP 1.

Additional Specific Assessment Core

Competencies 8 - 13

REGT 2.

Now available to support commercial medium pressure installations to the requirements specified in IGE/GM8

(Applicable to CESP1. & /or CMA1. &  MET4.)

Meter Installer CMA 2LS (Limited Scope)

Meter Installer

CMA 1.

Emergency Service

Provider CESP 1.

Domestic Meter

MET 1.

Gas Meter MET 3LS. (Limited Scope)

Medium Pressure

REGT 1.

Additional Options

With CMA 1.

Medium Pressure Installations REGT1.

Dom/Com Meter

MET 4.

Testing up/to 1m³

TPCP 1A

Part A: Generic Competencies must be completed by all candidates

Testing up/to 16 bar

TPCP 1.

Part B: Specific Competencies CMA1 & CESP1 only

RPD & Turbine

CMET 2.

Diaphragm/RPD

CMET 1.

Medium Pressure

REGT 2.

RPD & Turbine

CMET 2.

Diaphragm/RPD

CMET 1.

Medium Pressure

REGT 2.

Non/Dom Pipe

ICPN 1.

*SEE FLOW CHART

INITIAL EMERGENCY & METER INSTALLERS

*SEE FLOW CHART

INITIAL EMERGENCY & METER INSTALLERS

*SEE FLOW CHART

INITIAL EMERGENCY & METER INSTALLERS

*SEE FLOW CHART

INITIAL EMERGENCY & METER INSTALLERS

HTR1. Gas Space Heaters

CKR1. Gas Cookers

CEN1. Wet Central Heating

CCN1. Domestic Gas Core

ACS Re-Assessments to renew currently held assessments.

Renewed Re-assessment

CORE & 4 Assessments packaged together

CCN1.

+

CENWAT.

+

CKR1.

+

HTR1.

+

CPA1.

ACS Assessments currently held by operative & now requiring renewal

Operative seeks extension to scope of work activities

Not previously held

HWB1.  Water Boilers (Swimming pool)

Operative applies for new ACS Competence Certificate

HWB1.

WAT1. Instantaneous Water Ht.

Operative Takes Initial Assessment

Operative shows original initial ACS Certificates of Competence to Assessment Centre & applies for

re-assessment

Note: Re-Assessment only available for those operatives who renew their expired ACS assessments within 12 months of initial assessments expiring

GROUP 1. Generic LPG Reassessment Core Part A.

CCLP1.

Permanent Dwellings (PD)                            Residential Park Homes (RPH)

Leisure Accommodation Vehicles (LAV)   Boats Yachts/Other Vessels (B)

GROUP 2. Limited Scope Specific Sector

LPG Reassessment Core Part A.  Competencies

Includes Cabinet Heaters

CCLP1. (MC) & CABLP1.

GROUP 2. Limited Scope Specific Sector

LPG Reassessment Core Part A.  Competencies

Includes Vessels (Single supply)

CCLP1. (EP) & VESLP1.

Part B.

Specific Sector

Competencies

Permanent Dwellings (PD)

Black Print

Part B.

Specific Sector

Competencies

Boats, Yachts & Other Vessels (B)

Blue Print

Part B.

Specific Sector Competencies

Leisure Accommodation

Vehicles (LAV)

Gold Print

Part B.

Specific Sector

Competencies Residential Park Homes (RPH)

Dark Red Print

GROUP 2. LPG Reassessment from:-

LEI1.

Leisure equipment (Single bottle supply)

GROUP 2. LPG Reassessment from:-

VESLP2.* - EFJLP1.

* Operatives requiring to test & commission

pipework installed under VESLP2. will also

require Assessment TPCP1.

Selected Appropriate Domestic Appliance Re-Assessments from LPG Banks A/B

Options from VESLP1. - VESLP2. - EFJLP1. - TPCP1.

GROUP 2 Part A (EP)

1. Vessel locations & Safety Requirements

2. Supply Pressures, Emergency/Flow controls

3. Test for Soundness as per BS 5482 pt 1

4. Installation of External Pipework/Fittings

5. Identification of Unsafe Situations.

GROUP 2. Part A. (MC)

1. Characteristics of combustion – LPG

2. Ventilation Requirements

3. Installation of Pipework/Fittings

4. Identification of Unsafe Situations

5 Inspect & commission mobile cabinet heater

No Further Options

Options – Changeover Core LPG to NG CoLPNG1.

Those Holding RPH, LAV, and B. will require additional competencies to those holding (PD)

Re-Assessment Core Competencies

Generic Non-Domestic Re-Assessment Core

Commercial Appliance Installers Competencies

Part A.

Limited Scope Non-Domestic

Re-Assessments

There is no Core-required for the 2

re-assessments listed below which are designed for operatives who do not connect to a live gas supply

ICPN 1LS.

First fix Commercial Pipework

ICAE 1LS.

First fix Commercial

Appliances

Option EFJLP 1.

Options EFJLP 1. BMP 1.

CCCN 1.

Specific Part B

Re-assessment

Commercial Catering Core Competencies

Re-assessment selected from:-

COMCAT 1.

COMCAT 2.

COMCAT 3.

COMCAT 4.

COMCAT 5.

COCN 1.

Specific Part B

Re-assessment

Commercial Heating Core

Competencies

Re-assessment

selected from:-

CORT 1.

CIGA 1.

CDGA 1.

CGFE 1.

Separate

CCP 1.

CCLNG 1.

Specific Part B

Re-assessment

Commercial Laundry Core

Competencies

Re-assessment CLE 1.

Options

ICPN 1.

TPCP 1A.

TPCP 1.

Options

ICPN 1. TPCP 1A. TPCP 1.

EFJLP 1. BMP1. HWB 1. (Commercial)

Options

ICPN 1.

TPCP 1A.

TPCP 1.

Non-Domestic Re-Assessment Core

Pipe Installer/Commissioner COCNPI 1LS.

Competencies

Part A1.

Re-Assessments to complete COCNPI 1LS.

Must Include

ICPN 1. TPCP 1A. &/or TPCP 1.

Part A1.

1.   Identification of Unsafe Situations, Use of Emergency Notices for Pipework

2.   The Operation & Positioning of Emergency Isolation Controls & Valves

3.   Gas Emergency Actions & Procedures

PART A.

- Installation of Pipework & Fittings for Appliance Connections

- Tightness Testing of Appliance Pipework Connections

- The Operation & Positioning of Emergency Isolation Controls & Valves

- The Operation & Checking of Appliance Gas Safety Devices & Controls

- Checking & Setting Commercial Supply/Appliance &  Meter Regulators

- Identification of Unsafe Appliance Situations

PART B.

10.  Commercial Laundry Flueing requirements

- Commercial Laundry Ventilation requirements

- Appropriate Appliances

PART B.

- Commercial Heating Flueing requirements

- Commercial Heating Ventilation requirements

- Characteristics of Combustion with Forced Draught Burners

- Appropriate Appliances

PART B.

- Commercial Catering Flueing requirements

- Commercial Catering Ventilation requirements

- Appropriate Appliances

N.B. Re-assessment for Assessments TPCP 1. & TPCP 1A. will be fully assessed to the same new criteria as initial assessment as both normative documents supporting these assessments were significantly re-written & re-introduced in 2004/5, resulting in new & additional criteria not previously being assessed.

GROUP 1

GROUP 2

GROUP 3

NON DOMESTIC/COMMERCIAL ACS RE-ASSESSMENT CRITERIA

Re-assessment Changeover Core NG/LPG CoNGLP1. Generic Competencies 1-3

            - 1.  LPG Supply Pressures, Operation of & Positioning of Emergency Isolation Flow Controls &

            - Valves for Cylinders.

2.  Installation of Pipework & Fittings for LPG (Range of pipe sizes 6mm to 28mm).

3. Testing for Soundness LPG) Installation pipework with total volume as per BS 5482 pt. 1

operating pressure up to 37mbar.

Additional competencies to support fuel changeover for ‘Permanent dwellings’ (PD)

4.  LPG Medium Pressure Supplies, Isolation, Flow Controls & Valves for Gas Storage Vessels

5.   Installation of Pipework and Fittings for Liquefied Petroleum Gas

(Range of Pipe Sizes: 6mm to 28m)

Re-Assessment Generic Core

Competencies Part A.

RPD & Turbine

CMET 2.

Diaphragm/RPD

CMET 1.

Non/Dom Pipe

ICPN 1.

Testing up/to 16 bar

TPCP1.Same as Initial

Testing up/to 1m³

TPCP1A. Same as Initial

Dom/Com Meter

MET 4.

Medium Pressure

REGT 1. Same as Initial

Domestic Meter

MET 1.

Additional Options

With CESP 1.

Additional Re-Assessment Specific Core

Competencies Part B.

REGT 2.

Now available to support commercial medium pressure installations to the requirements specified in IGE/GM8

(Applicable to CESP1. & /or CMA1. & MET4.)

Meter Installer Re-Assessment CMA 2LS (Limited Scope)

Gas Meter Installer CMA 1.

Emergency Service

Provider CESP 1.

Additional Options

With CMA 1.

Medium Pressure

REGT 1. Same as Initial

Domestic Meter

MET 1.

Dom/Com Meter

MET 4.

Testing up/to 1m³

TPCP1A.Same as Initial

Testing up/to 16 bar

TPCP1.Same as Initial

Non/Dom Pipe

ICPN 1.

Diaphragm/RPD

CMET 1.

RPD & Turbine

CMET 2.

Gas Meter Re-Assessment MET 3LS. (Limited Scope)

CMIT 1.

Separate stand alone Limited Scope Re-assessment which includes its own core for

Meter Instrumentation Technicians

Medium Pressure Installations REGT1.

Same as Initial

Part A: Generic Competencies 1-5 (must be completed by all candidates)

Part B: Specific Competencies 6-10 (CMA1. & CESP1. only)

POLYETHLENE ELECTRO FUSION JOINTING EFJLP 1.    NG & LPG

This assessment is valid with the following core gas safety assessments:-

- In conjunction with both Domestic NG &/or LPG Cores (CCN 1.–CCLP 1.–CoNGLP 1.) Normal Route

- In conjunction with both any other core.

- On its own for limited scope operatives not connecting to a live gas supply (No pre-requisite required)

DOMESTIC APPLIANCES - NG & LPG                                       NG & LPG

(Cookers, Hot Water/Central Heating Boilers, Water Heaters)

This assessment is valid with the following core gas safety assessments:-

- In conjunction with both Domestic NG &/or LPG Cores (CCN 1.–CCLP 1.–CoNGLP 1.) Normal Route

- Limited scope (occasional involvement from appliance isolation valve to appliance in commercial environment ) in conjuction with Commercial l/Commercial Catering

(COCN 1. - CoDNCO 1. – CoNGLP 1. – CCCN 1. - CoDC1.)

TESTING & PURGING PIPEWORK                          TPCP 1A.          NG

(Not exceeding 1m³ volume)

TESTING & PURGING PIPEWORK                          TPCP 1.     NG & LPG

(Exceeding 1m³ volume)

This assessment is valid with the following core gas safety assessments:-

- In conjunction with both Commercial NG &/or LPG Cores (COCN 1.–CoDNCO 1.–CoNGLP 1.)

- In conjunction with any other Core 				                              Normal Route

This assessment is valid with the following core gas safety assessments:-

- In conjunction with the Commercial NG Core (COCN 1.)                                                    Normal Route

- In conjunction with any other NG Core

What areas of gas work do you undertake?

Use domestic NG flow chart to advise  candidate

Refer to non –domestic changeover flowchart to advise candidate which assessment to take.

Advise the candidate that the commercial catering appliance categories will cease to be valid when the Core CCN1 assessment expires.

I hold ACoP 1-14 qualifications that are out of date.

What ACS assessments do I need to take?

I hold CCN1 & CKR1 and wish to take a “changeover” assessment to extend my scope of work to include commercial catering appliances

Enquire as to which (if any) ACS assessments the operative holds and refer to page 8 flowchart.

## Note: If uncertain about any assessment requirements contact CORGI ACS Team on 01256 372291 or 372284

Which ACS assessments do I need to take to enable me to work on Mobile Catering Equipment?

Use domestic NG flow chart to advise the candidate

to undertake suitable changeover assessment

I carry out work on NG domestic cookers and hold CCN1 & CKR 1, however; I need to be able to carry out this type of work on LPG.

What assessment do I need to take?

Enquire as to which (if any) ACS assessments the operative holds & refer non-domestic flowchart

Which ACS assessments do I need to take to enable me to work on Mobile Catering Equipment?

What gas appliances do you carry out gas work on?

Use page domestic LPG chart to advise candidate, which core & sector assessment to take.

Use page domestic NG & LPG flow charts to advise candidate

which appliance assessments to take.

I work on Touring Caravans,

Residential Park Homes and Boats.

What ACS assessments do I need to take?

Use non-domestic flow chart to advise the candidate to undertake suitable core and appliance/equipment assessments

I install test & purge large commercial pipework, install & commission commercial

Overhead Radiant Tube Heaters.

What ACS assessments do I need to take?

NOTE:

If uncertain about any assessment requirements contact

Energy & Utility Skills Ltd.

Tel. No.

0845 077 99 22

Ensure the candidate is a “Limited Scope” operative and refer to the non-domestic flow chart

I install commercial pipe-work & appliances but do not connect to a live gas supply or commission the equipment.

What ACS assessments do I need to take?

Enquire as to whether the candidate carries out work on behalf of a Gas Transporter (GT) Meter Asset Manager or Gas Supplier & is approved by an OAMI registered business.

If so refer to ESP flowcharts to advise andidate which assessments to take.

I only install domestic gas meters up to U16 size.

What assessments do I need to take?